This form must be submitted for any Class 1 or Class 2 rocket project expected to reach 23,000’ AGL or 
greater in altitude and to be launched at the Argonia Rocket Pasture during any KLOUDBusters launch event. 
E-Mail completed form to prefect@kloudbusters.org a minimum of 30 days prior to the desired launch date.

Please provide all applicable information with as much detail as possible.

| Launch Site: Argonia, Kansas Rocket Pasture | Planned Launch Date: _____Friday September 1, 2023_________ |
| --- | --- |

- Flyer Data:

| Flyers’ names and addresses. For a group, list the primary flyer first, use additional pages as needed. | TRA or NAR member number(s) All group members must be current TRA or NAR members. | TRA/NAR Certification Level |
| --- | --- | --- |
| Freddy WILLEMS | NAR 97232 | 3 |
| 77 Dundee Pl. |  |  |
| St. Johns Florida 32259 |  |  |

- Rocket Data:

| Rocket name | PROJECT X | Kit name and Manufacturer (or “Scratch built”) | Scratch built |
| --- | --- | --- | --- |
| If not a kit, briefly describe the rocket airframe (i.e. 3 FNC, scale model, upscale from kit, important features, etc.) | Fiberglass // Booster 60” long 4” diameter – transition to 3” upper body tube 24” long – nose cone 15” long |
| Rocket Height (feet/inches) | 102” | Diameter (inches) | 4” to 3” |
| Rocket Weight without motors (lbs.) | 11.4 lbs | Weight with all motor(s) (lbs.) | 29.4 lbs |
| Drogue (describe) | 130 feet streamer |
| Main parachutes (describe) | 75” X- Form chute |
| Deployment method & charge | Stratologgers (2) Main 2 charges 1.8 and 2.0 – back up charges 2.0 and -streamer charges at APO and main chute charges at 700 feet |
| Electronics (if more than one device is used, provide manufacturer and model of each) | Stratologgers I Main and II Back Up |
| Initial thrust, in pounds | 3357.4 N3357.4 N (754.7 lbs MAX) | Thrust to Weight Ratio | 17.7 Average calculation |
| Other detailed rocket information: i.e. airframe materials, previous launches, simulation or mock-up data, etc. |
| This rocket flew at SRA field on Saturday May 15, 2021 to 7667 feet @ 727 MPH, winds were 12 Mph. Recovery was at 1.800 feet away. Motor was a L910 C STAR (CTI). Website of this flight with all data and lots and lots of video and pictures of this flight: https://www.insanerocketry.com/main/displayevent/4879279425252247612/ Website of the complete detailed building process: https://www.insanerocketry.com/main/display/8794511770789169384/?im7a0c61dc36e148e8page=8#im7a0c61dc36e148e8PageLinks |

- Propulsion Data:

|  | Number of motors | Manufacturer (or “Research”) | Motor Designation (e.g., N2000) | Propellant Weight | Total Impulse N-s |
| --- | --- | --- | --- | --- | --- |
| Main Motor(s) | M2245 IMAX | Cesaroni | CTI 99797 M2245 | 5074 grams | 9976.7 N-s |
| Add’l motors |  |  |  |  |  |
| Add’l motors |  |  |  |  |  |
| Airstarts |  |  |  |  |  |
| Second stage** |  |  |  |  |  |
| Third stage** |  |  |  |  |  |
| TOTAL INSTALLED Propellant Weight / Impulse N-s | 8182 grams |  |
| Describe each Research Motor: diameter, designation (J200, etc.), type and number of grains, propellant description, anticipated pressure, etc. Motors of less than 10240 N-s may be described very briefly. For larger motors, a printout from a motor modeling program is expected. Additional information (casing wall thickness, specific propellant formulation, etc.) is also expected for such motors. Use additional pages as needed. |
| The M2245 Imax motor is a 6 XL grain motor made by Cesaroni Technologies. |

**Staging Detail – Required for multiple stage rockets. For all staged flights, describe the sustainer ignition inhibit logic and settings used in the event of a non-optimal booster motor burn or non-optimal rocket trajectory

- Ignition and Launch System Data:

| Rail/Rod type and length required | Rail 10/10 |
| --- | --- |
| Motor ignition description and sequence (if applicable) | ignitor |

- Simulation Data:  Results from (data should be included from each program or simulation actually used)

| Simulation estimation methods (one is required, two are better) | RockSim | RAS Aero | OpenRocket |
| --- | --- | --- | --- |
| Cd (coefficient of drag) |  |  | 7.1 |
| Stability margin (in calibers) |  |  | 1.3 |
| Velocity (ft/s): At top of launcher |  |  | 102 ft/sec |
| Maximum Velocity |  |  | 2366 ft/sec |
| Maximum altitude (ft) |  |  | 25929 feet |
| Will staging occur at > Mach 1.0? (Y / N / Not Applicable) |  |  |  |

Submitted: __07__/____01/____2023	Received: ____/____/____	KBoD approved: ____/____/____